## Slide 1: MUSCLE ACTIVATION PROJECT
Risheekesh Kesavan, Pratiksha Ganesan, Mikayla Schneider, Ravesh Sukhnandan

## Slide 2: INTRODUCTION
Each joint in the human body has a number of kinematic degrees of freedom, and each action can be performed in different ways using different combinations of muscles to achieve the same joint torque needed for this movement.
Experimental studies have found significant similarity in these muscle activation patterns for different individuals.
Modelled simulations can be applied to predict changes of kinematics and muscle response to interventions or environmental changes. They can support decisions in orthopaedic surgery.
[1] Which Muscles Are Used When Riding a Bike?, (Mar. 30, 2017). [Online Video]. Available: https://www.youtube.com/watch?v=MqLHuwxB5-c
APPLICATIONS OF MUSCLE MODELLING:
Modelling and Simulation of human biomechanics
Physical therapy/orthopedic surgery
Optimizing sports performance
Robotics
PROBLEM STATEMENT:
We aim to optimize the lower limb muscle activations during cycling by using external applied forces and kinematics from literature.
Notes: The human body has more muscles that it does degrees-of-freedom. An example of this is looking at the lower limbs. The knee for instance is a single degree of freedom joint, but yet there are many muscles spanning it. For example the quadriceps that extend the knee and the hamstrings that flex the knee. How does the body decide what muscle(s) to activate to perform a given task? This is an important question to answer because it has implications across a variety of different fields. By modelling and simulating human biomechanics, we can use this information to guide physical therapy and surgery for muscle dysfunction. We can also optimize sports performance. Finally, this may also have applications to robotics, where using these neuromuscular control strategies to control a highly redundant system remains very difficult.
Each joint in the human body has a number of kinematic degrees of freedom, and each action can be performed in different ways using different combinations of muscles to achieve the same joint torque needed for this movement.
Experimental studies have found significant similarity in these muscle activation patterns for different individuals.
Modelled simulations can be applied to predict changes of kinematics and muscle response to interventions or environmental changes. They can support decisions in orthopaedic surgery.

## Slide 3: PROBLEM STATEMENT
Problem Statement:
We aim to optimize the lower limb muscle activations during cycling by using external applied forces and kinematics from literature.
Notes: The particular application that we want to explore is that of cycling, which is amenable to analysis because the motion happens in a 2D plane and exhibits muscle redundancy. On the image on the left, you’ll notice that multiple muscles are being activated in red as the cyclists pedals the bicycle. Understanding which muscles are active when may be framed as an optimization problem. Our problem statement is that we aim to optimize the lower limb muscle activations during cycling by using joint kinematics and kinetics from literature, and compare to previously gathered EMG data.

## Slide 4: MODELLING
Minimize the metabolic cost of cycling, using the sum of squared activations as a proxy
Constrained by the moment required at each joint to produce the external force on the pedal
OBJECTIVE FUNCTION:
Table 1: Model Parameters
Notes: defining your optimization problem statement with equations and words- Pratiksha/Mikayla

## Slide 5: CLASSIFICATION OF OBJECTIVE FUNCTION
Algorithm | Time | Minimizer | Exitflag
SQP | 0.008 seconds | [0.18; 0.32; 0.1; 0.1; 0.63; 0.1] | 1
Interior point | 0.021 seconds | [0.18; 0.32; 0.1; 0.1; 0.63; 0.1] | 1
Problem | Convex objective, linear constraints, making it a convex problem
Solution | Global minimum
Algorithm choice | SQP (deals better with lot of constraints)
Algorithm comparison:
Notes: As we have a lot of inequality constraints, we preferred sqp over interior point as fmincon sqp also uses active set strategy to focus on the important constraints

## Slide 6: Data Flow for getting torques at joints
Pedal forces in the x- and y- direction
(Kautz et al.)
[1] “CYCLING DATA,” International Society of Biomechanics. https://isbweb.org/resources/data-resources/140-movement-data/510-cycling-data
Knee Torque
Hip Torque
Ankle Torque
Optimization
Muscle Activations
x
y
z
Notes: Ravesh

## Slide 7: Solution to the muscle redundancy problem shows reasonable muscle forces
Notes: Show force on slide 6. Slide 7 show activation

## Slide 8: Pedal Forces and Joint Torques vs. Activation
x
y
z
Notes: Add picture of the leg (mirrored horizontally)

## Slide 9: SOLUTIONS AND LAGRANGE MULTIPLIERS
Notes: Include units of Lagrange multipliers

## Slide 10: LB SENSITIVITY ANALYSIS: -30% Change
f (N*m) | λ | 0° | λ | 90° | λ | 180° | λ | 270°
LBRF | 0 | 0 | + | 1.5 | 0 | 0 | 0 | 0
LBIL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LBGL | + | 13.7 | + | 0 | + | 1.3 | + | 20.0
LBHA | + | 21.3 | 0 | 12.2 | + | 20.1 | + | 22.4
LBTA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LBGA | + | 7.8 | + | 4.5 | + | 12.1 | + | 6.0

## Slide 11: PARAMETER SENSITIVITY ANALYSIS: Θ = 90
Variable Changed | -30% Change |  |  |  |  |  | +30% Change |  |  |  |  | 
a (unitless) | %Δ in RF | %Δ in IL | %Δ in GL | %Δ in HA | %Δ in TA | %Δ in GA | %Δ in RF | %Δ in IL | %Δ in GL | %Δ in HA | %Δ in TA | %Δ in GA
Fmax,RF | 0 | 0 | 5.3 | 0 | 0 | 0 | 0 | 0 | -5.3 | 0 | 0 | 0
Fmax,IL | 0 | -42.9 | 0 | 0 | 0 | 0 | 0 | 23.1 | 0 | 0 | 0 | 0
Fmax,GL | 0 | 0 | -42.9 | 0 | 0 | 0 | 0 | 0 | 23.1 | 0 | 0 | 0
Fmax,HA | 0 | 8.8 | 0 | 0 | 0 | 0 | 0 | -8.8 | 0 | 0 | 0 | 0
Fmax,TA | 0 | 0 | 0 | 0 | -42.9 | 0 | 0 | 0 | 0 | 0 | 23.1 | 0
Fmax,GA | 0 | 0 | 0 | 0 | 9.8 | 0 | 0 | 0 | 0 | 0 | -9.8 | 0

## Slide 12: PARAMETER SENSITIVITY ANALYSIS EXAMPLE
Notes: Report peak activation as function of percent change in max muscle force

## Slide 13: INTERPRETATION | FORCE-LENGTH RELATIONSHIP
Prilutsky et al. EMG Data
Our Activation Profiles
Model Limitations
Number of Muscles
  Biarticular
Joint Kinematics
Parameters
2D vs. 3D
Objective Function
Nonlinear Force-Length-Velocity Relationship
[1] B. I. Prilutsky and R. J. Gregor, “Analysis of muscle coordination strategies in cycling,” IEEE Transactions on Rehabilitation Engineering, vol. 8, no. 3, pp. 362–370, Sep. 2000, doi: 10.1109/86.867878.
Notes: - Mikayla

## Slide 14: CONCLUSIONS FUTURE WORK
We were able to solve the muscle redundancy problem to get the muscle activations
While the activations were reasonable, they do not exactly match measured EMG profiles of cyclists.
A better match to the measured EMG could be done by increasing the realism of the model:
  Implementing realistic muscle characteristics such as force-length, force-velocity and activation dynamics
  Including the dynamics of motion instead of using a quasi-static assumption
  Minimizing a different objective function such as one that promotes distribution of muscle forces in the leg muscles

## Slide 15: Backup Slides

## Slide 16: INTERPRETATION
Prilutsky et al. EMG Data
Our Activation Profiles
Notes: - Mikayla