## Slide 1: Muscle Activation Project

## Slide 2: The human body has more muscles than it does degrees-of-freedom (DOF)
Each joint in the human body has a number of kinematic degrees of freedom, and each action can be performed in different ways using different combinations of muscles to achieve the same joint torque needed for this movement.
Experimental studies have found significant similarity in these muscle activation patterns for different individuals.
Modelled simulations can be applied to predict changes of kinematics and muscle response to interventions or environmental changes. They can support decisions in orthopaedic surgery.
Physical therapy/orthopaedic surgery
Modelling and Simulation of human biomechanics
Optimizing sports performance
Robotics
[1] Which Muscles Are Used When Riding a Bike?, (Mar. 30, 2017). [Online Video]. Available: https://www.youtube.com/watch?v=MqLHuwxB5-c
Notes: The human body has more muscles that it does degrees-of-freedom. An example of this is looking at the lower limbs. The knee for instance is a single degree of freedom joint, but yet there are many muscles spanning it. For example the quadriceps that extend the knee and the hamstrings that flex the knee. How does the body decide what muscle(s) to activate to perform a given task? This is an important question to answer because it has implications across a variety of different fields. By modelling and simulating human biomechanics, we can use this information to guide physical therapy and surgery for muscle dysfunction. We can also optimize sports performance. Finally, this may also have applications to robotics, where using these neuromuscular control strategies to control a highly redundant system remains very difficult.
Each joint in the human body has a number of kinematic degrees of freedom, and each action can be performed in different ways using different combinations of muscles to achieve the same joint torque needed for this movement.
Experimental studies have found significant similarity in these muscle activation patterns for different individuals.
Modelled simulations can be applied to predict changes of kinematics and muscle response to interventions or environmental changes. They can support decisions in orthopaedic surgery.

## Slide 3: Problem Statement
Problem Statement:
We aim to optimize the lower limb muscle activations during cycling by using external applied forces and kinematics from literature.
Notes: The particular application that we want to explore is that of cycling, which is amenable to analysis because the motion happens in a 2D plane and exhibits muscle redundancy. On the image on the left, you’ll notice that multiple muscles are being activated in red as the cyclists pedals the bicycle. Understanding which muscles are active when may be framed as an optimization problem. Our problem statement is that we aim to optimize the lower limb muscle activations during cycling by using joint kinematics and kinetics from literature, and compare to previously gathered EMG data.

## Slide 4: Problem Statement, cont
Minimize the metabolic cost of cycling, using the sum of squared activations as a proxy
Constrained by the moment required at each joint to produce the external force on the pedal
Notes: defining your optimization problem statement with equations and words

## Slide 5: describing your choice of solution algorithm
Our objective function is convex with linear constraints making it a convex problem.
Our solutions are global minima
Algorithm chosen -> SQP
Reason: SQP used a active set strategy. With many nonlinear constraints, we chose this algorithm to reduce processing time.
Notes: As we have a lot of inequality constraints, we preferred sqp over interior point as fmincon sqp also uses active set strategy to focus on the important constraints

## Slide 6: Solution to the muscle redundancy problem shows reasonable muscle activations for the IP, H and TA muscles

## Slide 7: Activations of IP, G and TA follow hip, knee and ankle torque profiles

## Slide 8: One Full Solution

## Slide 9: Sensitivity Analysis
Report peak activation as function of percent change in max muscle force

## Slide 10: Interpretation
Model Limitations
  Number of Muscles, particularly biarticular
  Joint Kinematics
  Parameters
  2D
Future Work
  Nonlinear Force-Length-Velocity Relationship
  3D

## Slide 11: Other: Force-Length Relationship (Interpretation)

## Slide 12: Conclusions Future Work
We were able to solve the muscle redundancy problem to get the muscle activations
While the activations were reasonable, they do not exactly match measured EMG profiles of cyclists.
A better match to the measured EMG could be done by increasing the realism of the model:
  Implementing realistic muscle characteristics such as force-length, force-velocity and activation dynamics
  Including the dynamics of motion instead of using a quasi-static assumption
  Minimizing a different objective function such as one that promotes distribution of muscle forces in the leg muscles